## Slide 1
Glider
Landing Gear
Warning Systems
Explanations, Guidance, and Animation
Updated: September 29, 2025

## Slide 2
This presentation may have been updated with new information, changes, and/or corrections.
Be sure to visit my presentation web site and download the latest version of this document. It could make an important difference to your work!
http://aviation.derosaweb.net/presentations
Thank you, John (OHM Ω)
Please Note #1

## Slide 3
There is no single universal answer on how
to implement a landing gear warning system in a particular glider. This is due to gliders having many different linkage designs to raise/lower landing gear and to open/close airbrakes. Hopefully, this presentation will provide enough information and pointers to help you design, install, and test a landing gear warning system for your glider.
Please Note #2

## Slide 4
Table of Contents
Learning How Gear Warning Works
Gear Warning Animation
Hardware Devices
Implementation
Testing the System

## Slide 5
LEARNING HOW A
LANDING GEAR
WARNING SYSTEM WORKS

## Slide 6
The basic electrical circuit for a landing gear warning system is very simple indeed.
The circuit consists only of a battery, some wires, two switches, and an alarm horn. See the circuit diagram below.
For each phase of flight (launch, airborne and landing) the two switches (gear and airbrake) are either ON (closed) or OFF (open).
If both switches are ON (closed) then an alarm will sound.
See an animation of this sequence of the operation in a later slide.
Landing Gear Switch
Airbrake Switch
Battery
Alarm
Horn
+
_
ALARM!
Ground
Power
Power
Power
Learning How Landing Gear Warning Systems Work

## Slide 7
The Basics - If the landing gear is retracted and the airbrakes are open at the same time the alarm must sound
The Specifics - The position of the switches are very important such that;
  If the gear is retracted - even a small amount - this will cause the associated power switch to close and to “arm” the system*
  If the airbrakes are opened - even a small amount - this will cause the associated power switch to close and to “arm” the system*
If both #1 and #2 above are true (gear is retracted and airbrakes are open) then both warning switches are “armed” (closed) and the alarm will sound
Learning How Landing Gear Warning Systems Work
*What does “arm the system” mean? To “arm” something is to initialize a control system to make it ready for action but not made able to take that action as yet. Usually this is to prevent accidentally triggering an event.
Example – During a NASA missile launch the button launch is not armed until just before launch.
Only at the last moment the button is connected to power (armed) and only then pushing the launch button will work.

## Slide 8
Flow Chart of a
Gear Warning System
ALARM!
Air Brake Status?
Gear
Status?
Open
Closed
Down
Up
NO ALARM!
Gear Up AND Airbrake Open??
YES!
NO
ALARM!
START
Here

## Slide 9
Landing Gear Warning PowerPoint Animation

## Slide 10
ANIMATION of a Sailplane Landing Gear Warning System
… 3 Phases of flight (Take Off, Airborne, Landing)
… Actuations of airbrake and gear control linkage
… Positions of gear warning alarm switches on/off
Click to continue to the Animation 
A Sailplane Landing Gear Warning PowerPoint Animation
Which Demonstrates The …

## Slide 11
Animation of a Sailplane Landing Gear Warning System
The following animation is of a sample gear warning system. The mounting, placement, and type of
magnetic switches and associated magnets
for your glider may be different than shown.
Review the information in the other slides in this presentation to help to implement
your landing gear warning system.
Click here to continue to the Animation 

## Slide 12
The included animation in this presentation has NOT been tested with versions of PowerPoint prior to 2004 and you may experience issues. An option is for you to download & view the available MP4 version of this presentation.
Important Notes for OLDER VERSIONS of PowerPoint
See http://aviation.derosaweb.net/presentations/#gearwarning
Click here to continue to the Animation 

## Slide 13
This presentation is available as an MP4 Video enable to view the gear warning animation for those without Microsoft PowerPoint
or if experiencing issues with an older version of PowerPoint (prior to 2004).
The MP4 Video will run by itself and not pause at each slide. This may be too fast to study each slide’s information and, especially, for watching the animation.
After downloading the MP4 version please use the pause function of your video program to step though the slides to carefully watch the
various phases of the gear warning animation.
Important Notes for Non-PowerPoint Users
See http://aviation.derosaweb.net/presentations/#gearwarning

## Slide 14
To receive the full value out of this presentation it is best to use Microsoft PowerPoint (2004 or later)
to view as a presentation.
Download the file and hit F5 (function key 5)
to start the presentation & animation.
Important Notes for PowerPoint 2004 and Later
See http://aviation.derosaweb.net/presentations/#gearwarning
Click here to continue to the Animation 

## Slide 15
DO NOT REMOVE THIS SLIDE!
Important Animation Transition Slide!

## Slide 16
Power (+)
Power (+)
 Up
Gear Control Lever
Down 
Magnet
Phase 2: Airborne
Landing Gear Up
Airbrakes Closed
Phase 1: Take Off
Landing Gear Down
Airbrakes Closed
 Open
Phase 4: Landing
Landing Gear Down
Airbrakes Open
Animation of a Sailplane Landing Gear Warning System
N.C. Magnetic Switch
N.C.
Magnetic Switch
Switch On
Switch Off
Switch On
Battery
LANDING GEAR UP!!
Landing Gear Down
Airbrakes Open
Airbrakes Closed
AIRBRAKES OPEN!!
Animation is shown using normally closed (N.C.) magnetic switches
Gear Control Lever
Down 
Magnet
Airbrake Control Lever
Closed 
Magnet
Power (+)
Ground (-)
Alarm
Horn
+
_
Power (+)
Alarm
Horn
ALARM!
Phase 3: Landing
Landing Gear Up!
Airbrakes Open!
Alarm Sounds!
Power (+)
Switch Off
Click to Sequence Animation
Armed!
Landing Gear Switch
Air Brake Switch
Notes: Add “No Power”?

## Slide 17
DO NOT REMOVE THIS SLIDE!
Important Animation Transition Slide!

## Slide 18
Airbrakes Open
Airbrakes Closed
Airbrakes Open
Landing Gear Up
Landing Gear Down
Gear Control Lever
Down 
Magnet
Gear Control Lever
Down 
Magnet
Airbrake Control Lever
Closed 
Magnet

## Slide 19
Click Here to
Repeat
Animation
Click Here to
Learn
More

## Slide 20
LANDING GEAR WARNING SYSTEM HARDWARE DEVICES

## Slide 21
Magnetic switches are preferred because;
  Safety – To activate the magnetic switch the magnet does not need to touch each other. Thus, by not touching control linkages reduces the possible of linkage interference/damage and/or switch damage
  Nearly any magnet, large or small, will work to activate the magnetic switch
  The magnetic switch will last through many more millions of on/off cycles versus a mechanical switch
  The magnetic switch can be easily mounted (typically epoxied in place)
  The magnet can be mounted in various ways;
    Steel linkages: the magnet will attach itself (permanently glue later)
    Aluminum linkages: taped in place for testing (permanently glue later)
    Either mounting method allows for easily movement of the magnets to test the warning system’s functionality
Landing Gear Warning System Hardware
* See https://www.youtube.com/watch?v=R--m0NDR0j8&t=338s for an aviation related safety take on the use of mechanical micro-switches.
There are Typically Two Types of Switches Used in Gear Warning Systems
  Mechanical (Micro) switches
  Magnetic switches

## Slide 22
  Magnetic “Reed” Switches
    This is an electro-mechanical switch
    Uses a pair of magnetizable, flexible, metal reeds whose end portions are separated by a small gap
    https://en.wikipedia.org/wiki/Reed_switch
  Magnetic “Hall-Effect” Switches (Sensors)
    Requires power to work
    Less prone to mechanical failure due to no wear on physical parts
    https://en.wikipedia.org/wiki/Hall_effect_sensor
Landing Gear Warning System Hardware
Magnetic “Reed”
Magnetic “Hall-Effect”
There are Two General Types of Magnetic Switches

## Slide 23
Examples of Various Common Magnetic (Reed) Switches
Landing Gear Warning System Hardware
See https://en.wikipedia.org/wiki/Reed_switch
Most Basic Type (Glass Enclosed)

## Slide 24
Another Type of Magnetic Switch
  Another type of magnetic switch is known as a “Hall Effect Sensor”.
  It works similar to the previously mentioned “Reed” switch by being activated by a nearby magnet. An advantage is that the the hall effect sensor has no moving parts.
  Mounting of this sensor may be different than the “Reed” types.
  Wiring of this sensor will be different as shown in the sample diagram.
  See https://en.wikipedia.org/wiki/Hall_effect_sensor for details.
Landing Gear Warning System Hardware
Sample Circuit
Examples of Various Common Magnetic “Hall-Effect” Switches
See https://en.wikipedia.org/wiki/Hall_effect_sensor

## Slide 25
  Normally Open (N.O.) Magnetic Switch
    When a magnetic N.O. switch is near a magnet, electricity will flow through the wires (turned on)
    When a magnetic N.O. switch is not near a magnet, electricity will not flow through the wires. (turned off)
  Normally Closed (N.C.) Magnetic Switch
    When a magnetic N.C. switch is near a magnet, electricity will not flow through the wires. (turned off)
    When a magnetic N.C. switch is not near a magnet, electricity will flow through the wires. (turned on)
Landing Gear Warning System Hardware
Magnetic “Reed” Switch
Magnetic “Hall-Effect” Switch
For Gear Warning systems two switches will be required (air brake and landing gear). For your particular glider’s situation you may need one of each type of switch, or two switches of a particular type.
There are Two Common Types of Switch Contacts

## Slide 26
  Alarm Horn
    There are many 12Vdc alarm piezoelectric horns available on the internet.
    Get an alarm that is LOUD! The Mallory Sonalert brand of audible alarms is the best IMHO.
    Amazon link to Mallory Sonalerts  https://www.amazon.com/s?k=sonalert
    Typical mounting position of the horn is hidden behind the instrument panel.
Landing Gear Warning System Hardware
Alarm Horn, Wiring & Switches
  Wiring & Battery Connections
    Use only Tefzel type wiring
    See http://aviation.derosaweb.net/presentations/#wiring for more details.
  Magnetic Switches
    Secure mounting of the magnetic switch and magnet is critical.
    A high quality epoxy is the best option. West Systems brand is recommended.

## Slide 27
IMPLEMENTATION OF A LANDING GEAR WARNING SYSTEM

## Slide 28
Becoming Familiar with How the Gear Warning System Works
  Temporarily connect the magnetic switches to a battery and the alarm horn* as shown in the simple wiring diagram below
  Move magnets near/away from the magnetic switches to turn them on/off and see how this turns on/off the alarm horn.
IMPLEMENTING A LANDING GEAR WARNING SYSTEM
Landing Gear Switch
Airbrake Switch
Battery
Alarm
Horn
+
_
ALARM!
Ground
Power
Power
Power

## Slide 29
Trial Installation of the Gear Warning System
  Gain access to the gear and airbrake linkages by removing access panels as needed. Typically, these locations are nearest to the handles of the airbrake and gear levers along the sides of the cockpit.
  Determine how the gear and airbrake linkages move as the handles are push/pulled. The portion moving is where the magnets should be temporarily mounted* so that they move back and forth on the linkage and will actuate/deactivate a nearby magnetic switch.
  Temporarily mount* the magnetic switches so that when the handles+magnets move they come close enough to the magnetic switch to activate it (within appox. 1/8” or 3mm).
    You may find that a more powerful rare-earth magnet is needed in your particular glider
  Temporarily wire the switches to the battery and alarm horn per the previous slide.
* Double sided tape should work well during testing
IMPLEMENTING A LANDING GEAR WARNING SYSTEM

## Slide 30
Adding a Landing Gear Alarm Test Button
  It is always best to test the system by opening the airbrakes while cycling the landing gear. However, you may want to add a momentary type test button that bypasses both of the magnetic switches for testing purposes.
Momentary
Test Button
Landing Gear Switch
Airbrake Switch
Battery
Alarm
Horn
+
_
ALARM!
Ground
Power
Power
TESTTING A LANDING GEAR WARNING SYSTEM

## Slide 31
TESTING A LANDING GEAR WARNING SYSTEM

## Slide 32
Testing the Trial Gear Warning System
  Place the fuselage on a cradle to allow the gear to be easily raised and lowered
  Fully assemble the glider (wings, etc) for correct linkage movement
  Test sequence;
    Lower the gear and move the airbrakes to both open & closed positions The alarm horn should not sound
    Raise the gear and close the airbrakes The alarm horn should not sound
    Raise the gear and open the airbrakes The alarm horn MUST SOUND
  Adjustments if needed
    Type of switched used (normally open or normally closed)
    Wiring of switches to the battery and/or alarm horn.
    Positions of the switches and/or magnets
    Retest until correct.
IMPLEMENTING A LANDING GEAR WARNING SYSTEM

## Slide 33
Flow Chart for Testing
A Gear Warning System
ALARM!
Air Brake Status?
Gear
Status?
Open
Closed
Down
Up
NO ALARM!
Gear Up AND Airbrake Open??
YES!
NO
ALARM!
START
Here

## Slide 34
Click Here to
Repeat
Animation
Click Here to
End
Presentation

## Slide 35: See My Other Presentations
http://aviation.derosaweb.net/presentations
Let me know of any comments!
Glider Electrical Wiring
Transceiver Troubleshooting
Oxygen Systems
Working with Glider Air Lines
Trailer Wiring & LED Lighting
Trailer Chains
Soaring Pilot Relief Systems
Battery Testing
Emergency Location Devices
Survival Kits
Spar Alignment Tool
L’Hotellier Fittings
Carbon Fiber Panels
IGC Filename Decoding
Blanik L-23 Strut Work
Removing Painted Lettering
Open Glider Network
Instrument Knob Extensions
Landing Gear Warning Systems